## Slide 1: KY Work Zone Intrusion Overview for House Transportation Committee

## Slide 2: KENTUCKY WORK ZONE STATISTICS
Year Crashes Injuries Fatalities
2022 1,074 271 6
2021 1,252 299 10
2020 905 228 6
2019 1,251 323 8
2018 1,042 280 3
2017 1,007 233 12

## Slide 3: Work Zone Fatalities Caused by Distracted Drivers (2019 – 2021 U.S. Avg %)
Urban Roads
Interstates 13.7%
Principal Arterials 9.5%
Minor Arterials 6.6%
Local Roads 8.8%
Rural Roads
Interstates 19.6%
Principal Arterials 13.4%
Minor Arterials 13.6%
Local Roads 12.1%

## Slide 4: Columbia Gas of Kentucky Incidents (2023)
Date of Incident | Description
02/17/2023 | Team Fishel restoration crew had one lane closed on a residential roadway to replace concrete on a previous road cut. A driver turned from a side street, drove through the cones at less than 5 MPH, and into the 8" deep excavation and became stuck. Driver was unsure of why he drove into the work zone but admitted that it was his fault. There was no damage to the vehicle or site equipment and no injuries. The work zone was set up correctly. Team Fishel assisted the driver out of the excavation.
02/24/2023 | While setting up a work zone for a Miller Pipeline mainline installation, a Wright Traffic Control vehicle was sideswiped by a vehicle driving through the work zone. No injuries occurred. The Wright team had begun installing cones down the center line of the two-lane street but had not yet closed the lane or set up the taper when a vehicle entered the lane that was in the process of being closed and struck the side of the Wright vehicle while passing between the vehicle and the cones. While CKY management was on site to investigate the incident, two vehicles driving through the work zone were almost involved in a head-on collision because a side street was not being monitored by the flagging crew allowing a vehicle to turn onto the street into oncoming traffic. A work zone planning form had been completed for the work zone set up that morning but a new planning form was not completed when the work zone was moved to a new location in the afternoon. The work zone was not inspected as required by the NiSource Work Zone Protection policy and a shadow vehicle was not used to protect the area from intrusion during set up.
10/03/2023 | A CJ Hughes crew was installing main on a section of 6th Street between Harrison and Long Streets in Ashland, KY with heavy traffic volumes. The traffic control crew were allowing 15-20 cars through the work zone at a time and traffic had begun to back up. A driver in the middle of the waiting line of cars got out of the line and drove into the oncoming lane toward the work zone. When the driver realized the lane ahead was closed, they drove through the taper and down Harrison Street, which had been closed by the traffic control crew. The driver fled the scene. There were no injuries or equipment damage.

## Slide 5: Columbia Gas of Kentucky Incidents (2022)
Date of Incident | Description
07/19/2022 | Work was being completed by a Miller Pipeline crew at 19 Mentelle Park which caused one half of the street to be closed due to the dump truck obstructing the street. A resident at the adjacent address wanted to drive through the work zone to access their driveway but was directed by the flagger to travel down the street on the other side of the grassy median and make a U-turn to access their driveway from the other side of the work zone. The driver ignored the instructions of the flagger and another member of the crew informing her that she could not fit past the dump truck and continued onward, making contact with the dump truck. There were no injuries and the driver caused minor damage to their vehicle and no damage to the dump truck. Police were not contacted and no citation was issued. The driver admitted to the crew that they were impatient and that the incident was their fault.
08/18/2022 | A distracted driver was approaching the work zone where a lane had been closed and flaggers were controlling traffic when the driver slammed on their brakes and stopped before reaching the flagger with the stop paddle. The driver noticed a police vehicle that was behind them and then accelerated into and through the work zone, coming within two feet of the flagger. The police vehicle activated their lights and sirens and pursued the driver. There were no injuries. The driver was arrested nearby.
11/10/2022 | A contractor crew installing a service line had an open excavation in the street with a proper work zone set up. An intoxicated person drove a motorized scooter through the cones and into the open excavation. Police were already on scene and escorted the man from the work site. There were no injuries or property damage.