# AN ACT relating to boilers.

Be it enacted by the General Assembly of the Commonwealth of Kentucky:

# Section 1.   KRS 236.060 is amended to read as follows:

## (1)	KRS 236.005 to 236.150 shall not apply to boilers or pressure vessels or related piping under federal control.

## (2)	KRS 236.005 to 236.150 shall not apply to the following boilers or related piping:

### (a)	Boilers or pressure vessels located on farms and used solely for agricultural purposes;

### (b)	Boilers or pressure vessels located at any oil refineries;

### (c)	Boilers or pressure vessels located at any utility operating under a certificate issued pursuant to KRS 278.020, if the boilers or pressure vessels are inspected by a special boiler inspector under the provisions of KRS 236.110, except that the inspection interval provided for in KRS 236.110 shall be extended to eighteen (18) months;

### (d)	Steam or vapor boilers used for heating purposes carrying a pressure of not more than fifteen (15) pounds per square inch gauge, and which are located in private residences[ or in apartment houses of less than six (6) families];

### (e)	Hot water heating boilers carrying a pressure of not more than thirty (30) pounds per square inch gauge which are located in private residences[ or in apartment houses of less than six (6) families or hot water supply boilers which are located in private residences or in apartment houses of less than six (6) families];

### (f)	Any unfired pressure vessels used as containers for liquefied petroleum gases and subject to the jurisdiction of the Department of Housing, Buildings and Construction under KRS Chapter 234;

### (g)	Pressure vessels used for transportation of compressed gases if constructed and operated in compliance with specifications and regulations of another state or federal authority;

### (h)	Pressure vessels containing air located on vehicles operating under the regulations of another state or federal authority;

### (i)	Pressure vessels operating at a maximum pressure of fifteen (15) PSI or less;

### (j)	Single wall pressure vessels having an inside diameter of six (6) inches;

### (k)	Pressure vessels with a nominal water containing capacity of one hundred twenty (120) gallons or less, to be used for domestic supply purposes, for containing water under pressure, including those containing air, the compression of which serves only as a cushion;

### (l)	Pressure vessels containing water heated by steam or other indirect means when none of the following are exceeded:

#### 1.	Heat input of two hundred thousand (200,000) BTU/Hr.;

#### 2.	Water temperature of two hundred ten (210) degrees Fahrenheit;

#### 3.	Water storage capacity of one hundred twenty (120) gallons;

### (m)	Coil type hot water boilers without a steam space and where no steam is generated within the confines of the unit but where water flashes into steam when released to atmospheric pressure by the operation of a manually operated nozzle, unless one (1) of the following is exceeded:

#### 1.	Three quarter (3/4) inch inside diameter tubing or pipe size with no drum or header attached;

#### 2.	Six (6) gallon water containing capacity;

#### 3.	Three hundred fifty (350) degrees Fahrenheit water temperature;

### (n)	Water heaters which are directly fired with oil, gas, or electricity, when none of the following limitations are exceeded:

#### 1.	Heat input of two hundred thousand (200,000) BTU/Hr.;

#### 2.	A water temperature of two hundred ten (210) degrees Fahrenheit;

#### 3.	A water containing capacity of one hundred twenty (120) gallons;

### (o)	Pressure vessels which may be classified as:

#### 1.	Pressure containers which are integral parts of components of rotating or reciprocating mechanical devices such as pumps, compressors, turbines, generators, engines, and hydraulic or pneumatic cylinders where the primary design considerations or stresses are derived from the functional requirements of the device; or

#### 2.	Structures whose primary function is the transport of fluids from one location to another within a system of which it is an integral part, that is, piping system.

## (3)	The fees required by KRS 236.120(1) and 236.130 shall not apply to standard and miniature antique and hobby boiler-operated tractors and equipment used solely for exhibition, if the boiler uses a fifty (50) pounds per square inch or less gauge.

# Section 2.   KRS 236.120 is amended to read as follows:

## (1)	If, upon inspection, a boiler or pressure vessel is found to comply with the administrative regulations of the department, the owner, user, or insurance company of it shall pay to the department the sum of twenty-five[fifteen] dollars ($25)[($15)]. When the inspection is made by a special inspector, the inspector shall attach the certificate fee to his or her report. The chief boiler inspector, or his or her duly authorized representative, shall issue to the owner or user a certificate of inspection for the boiler or pressure vessel bearing the date of inspection and specifying the maximum pressure under which the boiler may be operated. An inspection certificate shall be valid for not more than fourteen (14) months from its date in the case of power boilers, and twenty-six (26) months in the case of low pressure steam or vapor heating boilers, hot water heating boilers, or hot water supply boilers. Certificates shall be posted under glass in the room containing the boiler inspected or, in the case of a portable boiler, shall be kept in a tool box accompanying the boiler.

## (2)	No certificate of inspection issued for an insured boiler, inspected by a special inspector, shall be valid after the insurance on the boiler for which it was issued terminates. Boilers shall be insured by a company duly authorized by this state to carry the insurance.

## (3)	The commissioner or his or her authorized representative may at any time suspend a certificate of inspection if, in his or her opinion, the boiler or pressure vessel for which it was issued cannot be operated without menace to the public safety, or if the boiler or pressure vessel is found not in compliance with this chapter or the administrative regulations of the department. A special boiler inspector shall have corresponding powers with respect to suspending certificates of inspection for boilers insured by the company employing him or her. The suspension of a certificate of inspection shall continue in effect until the boiler or pressure vessel conforms to this chapter and administrative regulations of the board, and until the inspection certificate is reinstated.

## (4)	A suspended certificate of inspection shall be reissued on the recommendation of the boiler inspector or special boiler inspector who first caused the suspension or at the discretion of the chief boiler inspector.

# Section 3.   KRS 236.210 is amended to read as follows:

## (1)	No person[, except contractor-installers of boilers operating at more than five hundred (500) pounds per square inch gauge or at more than four hundred sixty-seven (467) degrees Fahrenheit,] shall engage in the business of installing, erecting, or repairing boilers unless he or she first obtains a license from the commissioner on recommendation of the board.

## (2)	Each person, firm or corporation must pass an examination prepared by the board and administered by the department.

## (3)	A license shall be issued by the commissioner or the chief boiler inspector upon recommendation of the board and payment of a reasonable fee not to exceed the cost of examination and other expenses involved as established by the commissioner upon advice of the board pursuant to KRS Chapter 13A.

## (4)	The license shall be renewable annually, not later than the first of the month following the expiration date, upon payment of a reasonable fee not to exceed the costs involved in such renewal as established by the commissioner upon advice of the board pursuant to KRS Chapter 13A.

## (5)	All individuals in the employ of a licensee shall not be required to be licensed.