# AN ACT relating to on-site sewage disposal system permits.

Be it enacted by the General Assembly of the Commonwealth of Kentucky:

# Section 1.   KRS 211.350 is amended to read as follows:

## (1)	The cabinet shall regulate the construction, installation, or alteration of on-site sewage disposal systems except for systems that have a surface discharge.

## (2)	No person, firm, or corporation shall construct, install, alter, or cause to be constructed, installed, or altered, any on-site sewage disposal system subject to regulation by the cabinet without having first obtained an on-site sewage disposal permit from the local health department. In lieu of inspection and certification by the local health department a licensed professional engineer in private practice licensed by the Commonwealth of Kentucky may perform site evaluations and approve system designs for an on-site sewage disposal system for the person, firm, or corporation and apply for the permit from the local health department, which shall approve or deny the request for permit within fifteen (15) working days of the submission of the request and shall provide to the applicant, in the event of denial, all necessary information relating to requirements for approval and permitting of an on-site sewage disposal septic or alternative system installation by the local health department, or by another agency, in the event that the on-site disposal system required will involve a surface discharge. The final systems installation inspection shall be performed by the local health department within fifteen (15) working days of the owner's request to the local health department for a final inspection. All applicable provisions of KRS Chapter 322 shall govern the licensed professional engineer. A professional engineer shall not perform site evaluations, approve system designs, or certify system installations of an on-site sewage disposal system on property owned by himself, an employee, or a partner of an engineering firm by which he is employed, or on property owned by the engineering firm. Nothing in this section shall be construed to deny a farmstead owner the right to obtain a permit. Except for farmstead owners on their own property, the construction, installation, or alteration shall be performed only by a person certified by the cabinet pursuant to KRS 211.357.

## (3)	A local health department that issues a permit for an on-site sewage disposal system based on the site evaluation or system design of a licensed professional engineer in private practice licensed by the Commonwealth of Kentucky shall not be held liable for any defects or failures of the on-site sewage disposal system due to the site evaluation or system design.

## (4)	No person, firm, or corporation shall use or continue to use or permit the use or continued use of any on-site sewage disposal system that is constructed, installed, or altered under an on-site sewage disposal permit if the cabinet or local health department through a duly authorized inspector, employee, agent, or licensed professional engineer in private practice licensed by the Commonwealth of Kentucky finds that the system was not constructed, installed, or altered in conformance with the permit and regulations issued by the cabinet.

## (5)	No certified electrical inspector acting under authority of KRS 227.491 shall issue the certificates of approval of temporary or permanent electrical wiring unless the inspector has in his or her possession a notice of release as described in paragraphs (a) and (b) of this subsection. The inspector shall record the number of the notice of release on the certificate of approval. The person requesting approval of electrical wiring shall be responsible for obtaining the release from the local health department and providing it to the electrical inspector. This requirement shall only apply to dwellings, mobile homes, manufactured housing, buildings, or other structures that are constructed or installed after July 15, 1998. This requirement shall not apply to structures that do not have sewage waste fixtures or to those that are connected to a sewage waste disposal system approved by the Natural Resources and Environmental Protection Cabinet. Nothing in this section shall be construed to deny the continued use of any electrical service connected to wiring approved prior to July 15, 1998.

### (a)	An initial notice of release to allow temporary electrical power for construction shall be issued to the property owner or owner's agent by the local health department upon the application for a site evaluation. All such site evaluations shall be conducted within fifteen (15) working days of the submission of the request, regardless of weather conditions, and in all cases shall include a perk test soil evaluation prior to any determination that an alternative on-site sewage disposal system is to be required. If the evaluation determines that an alternative on-site disposal system having a surface discharge is necessary, thus requiring permitting by the Natural Resources and Environmental Protection Cabinet, the local health department shall forward all permit application information and evaluation documentation to the Natural Resources and Environmental Protection Cabinet on behalf of the owner, and the Natural Resources and Environmental Protection Cabinet shall conduct a site evaluation and make recommendations for sewage disposal system plans within fifteen (15) working days of receiving the permit and evaluation documents from the local health department.

### (b)	A final notice of release to allow for permanent electrical power shall be issued to the property owner or owner's agent by the local health department upon approval of an on-site sewage disposal plan not requiring a surface discharge. An on-site sewage disposal plan not requiring a surface discharge shall be processed and reviewed, and shall be either approved or denied by the local health department within fifteen (15) working days of its submission to the health department. Any alternative on-site sewage system plan containing plans for a surface discharge shall by approved or denied by the Natural Resources and Environmental Protection Cabinet within fifteen (15) working days of its submission.

### (c)	This section shall not apply to any county that has adopted the Uniform State Building Code and has and enforces on-site sewage disposal permitting.

## (6)	All applications for on-site sewage disposal permits shall be accompanied by plans and specifications for the proposed system, including results of soils tests and other information as directed by the cabinet by regulation. If the site evaluation or approval of the system design is performed by a licensed professional engineer in private practice licensed by the Commonwealth of Kentucky, the application shall be accompanied by a statement by the engineer that he has met the requirements of the regulations issued by the cabinet for site evaluation and system design. Any action to deny an application shall be subject to appeal, and upon appeal an administrative hearing shall be conducted in accordance with KRS Chapter 13B.

## (7)	The cabinet shall fix a schedule of fees for the functions performed by the cabinet relating to the regulation of on-site sewage disposal systems. The fees shall be designed to fully cover the cost of the service performed but shall not exceed the cost of the service performed. Fees payable to the cabinet shall be paid into the State Treasury and credited to a trust and agency fund to be used by the cabinet in carrying out its responsibilities relating to the regulation of on-site sewage disposal systems. No part of the fund shall revert to the general fund of the Commonwealth.

## (8)	Any regulation relating to on-site sewage disposal that is in effect on July 15, 1992, shall remain in effect until altered by the secretary. The secretary may issue additional regulations necessary to carry out the purposes of this section.

## (9)	Nothing in this section shall authorize or allow the cabinet to inspect or take enforcement action against on-site sewage disposal systems installed on farmsteads prior to July 15, 1992, or modifications to those systems unless the actions are determined in writing by the cabinet, upon a written, verified complaint, to be necessary to prevent imminent harm or damage to the safety, life, or health of a person. In this instance, the cabinet shall deliver to the landowner a copy of the written determination and the verified complaint prior to the commencement of the inspection or enforcement action.

# Section 2.   KRS 211.380 is amended to read as follows:

If a proposed site fails to meet the criteria established by the cabinet for a septic tank system, the owner shall be notified in writing within fifteen (15) working days of the soil evaluation, and provided with information relating to an alternative on-site sewage system alternative that can be approved, and a permit shall be granted for an approved on-site sewage disposal system other than a septic tank, including modified subsurface systems, mechanical systems, and any other system appropriate to the individual characteristics of the site which will provide sewage treatment that meets established water quality criteria and health standards. In the event the alternative on-site sewage system will require a surface discharge, and thus the approval and permitting of an agency other than a local health department, the health department shall, within fifteen (15) working days, submit, on behalf of the owner, all documentation regarding evaluation and possible alternatives to the appropriate agency for permit approval of on-site sewage systems with surface discharge.

# Section 3.   KRS 318.134 is amended to read as follows:

## (1)	No person, firm, or corporation shall:

### (a)	Construct, install, or alter, or cause to be constructed, installed, or altered, any plumbing without first having procured a plumbing installation permit therefor from the department;

### (b)	Use or continue to use, or permit the use or continued use of, any plumbing constructed, installed, or altered under a plumbing installation permit issued therefor where the department through a duly authorized inspector, employee, or agent, finds that the plumbing was not constructed, installed, or altered in accordance with such permit and the Kentucky State Plumbing Code.

## (2)	All applications for plumbing installation permits shall be accompanied by plans and specifications of the proposed plumbing installation, location, and construction of the water supply system to be used. The department shall have fifteen (15) working days from the date of submission to either approve or deny a permit for installation. If an on-site sewage disposal system that does not have a surface discharge is proposed, a valid on-site sewage disposal permit issued by the Cabinet for Health Services or its designated agent shall accompany the application.

## (3)	The department shall fix a reasonable schedule of fees and charges to be paid for plumbing installation permits and the necessary inspections incident thereto. The department shall also fix a reasonable schedule of fees and charges to be paid for necessary inspections of the construction, installation, or alteration of plumbing in public buildings.

# Section 4.   KRS 318.160 is amended to read as follows:

Except as otherwise provided by law or by regulation of the department, no person shall construct, install, or extensively alter any plumbing, sewerage, or water supply system of any public building or establishment without having first obtained the approval of the department in writing. Detailed plans and specifications of the proposed facility showing the plumbing system, sewage disposal system, and water supply system shall be submitted to the department prior to the construction or alteration of the facility. In the event no public sewer is available, the plan shall include the proposed type of sewage disposal system. In the event a sewage subsoil drainage system is used, or some other type of on-site sewage disposal system that does not have a surface discharge, the application for construction, installation, or alteration of such system shall be submitted to the Cabinet for Health Services or its designated agent. All other plans and specifications shall be submitted in triplicate to the department. The department shall notify the applicant in writing of the approval or disapproval of the plans within fifteen (15) working days of their submission. The construction, installation, or alteration shall be done in accordance with the approved plans.