# AN ACT relating to swimming pools.

Be it enacted by the General Assembly of the Commonwealth of Kentucky:

# SECTION 1.   A NEW SECTION OF KRS CHAPTER 198B IS CREATED TO READ AS FOLLOWS:

## (1)	A swimming pool, or other contained body of water that contains water eighteen (18) or more inches in depth at any point and that is wider than eight (8) feet at any point and is intended for swimming, shall be protected by an enclosure surrounding the pool area, as provided in this section.

## (2)	A swimming pool, whether a below-ground or above-ground pool, or other contained body of water required to be enclosed by subsection (1) shall meet the following requirements:

### (a)	Be entirely enclosed by at least a five (5) foot wall, fence, or other barrier as measured on the exterior side of the wall, fence, or barrier;

### (b)	Have no openings in the wall, fence, or barrier through which a spherical object four (4) inches in diameter may pass. The horizontal components of any wall, fence, or barrier shall be spaced not less than forty-five (45) inches apart measured vertically or shall be placed on the pool side of a wall, fence or barrier which shall not have any opening greater than one and three-quarter (1-3/4) inches measured horizontally. Wire mesh or chain link fences shall have a maximum mesh size of one and three-quarter (1-3/4) inches measured horizontally;

### (c)	Gates for the enclosure shall:

#### 1.	Be self-closing and self-latching with the latch located at least fifty-four (54) inches above the underlying ground or on the pool side of the gate with a release mechanism at least five (5) inches below the top of the gate and no opening greater than one-half (1/2) inch within twenty-four (24) inches of the release mechanism or be secured by a padlock or similar device which requires a key, electric opener, or integral combination which can have the latch at any height; and

#### 2.	Open outward from the pool;

### (d)	The wall, fence, or barrier shall not contain openings, handholds, or footholds accessible from the exterior side of the enclosure that can be used to climb the wall, fence, or barrier; and

### (e)	The wall, fence, or barrier shall be at least twenty (20) inches from the water's edge.

## (3)	If a residence or living area constitutes part of the enclosure required by subsection (2) of this section for a swimming pool or other contained body of water, in lieu of the requirements of subsection (2) of this section there shall be one (1) of the following:

### (a)	Between the swimming pool or other contained body of water and the residence or living area, a minimum four (4) foot wall, fence, or barrier to the pool area which meets all of the requirements of paragraphs (b) to (e) of subsection (2) of this section;

### (b)	A motorized safety pool cover that requires the operation of a key switch which meets the American Society of Testing and Materials standard F1346-91 and which does not require manual operation other than the use of the key switch;

### (c)	All ground-level doors or other doors with direct access to the swimming pool or other contained body of water shall be equipped with a self-latching device which meets the requirements of subdivision 1. of paragraph (c) of subsection (2) of this section. Emergency escape or rescue windows from sleeping rooms with access to the swimming pool or other contained body of water shall be equipped with a latching device not less than fifty-four (54) inches above the floor. All other openable dwelling unit or guest room windows with similar access shall be equipped with a screwed-in-place wire mesh screen, or a keyed lock that prevents opening the window more than four (4) inches, or a latching device located not less than fifty-four (54) inches above the floor; or

### (d)	An above-ground swimming pool which has nonclimbable exterior sides with a minimum height of four (4) feet. Any access ladder or steps shall be removable without tools and secured in an inaccessible position with a latching device not less than fifty-four (54) inches above the ground when the pool is not in use.

## (4)	This section does not apply to:

### (a)	A system of sumps, irrigation canals, irrigation, flood control, or drainage works constructed or operated for the purpose of storing, delivering, distributing, or conveying water;

### (b)	Stock ponds, storage tanks, livestock operations, livestock watering troughs, or other structures used in normal agricultural practices;

### (c)	Public or semipublic swimming pools;

### (d)	A swimming pool or contained body of water or barrier constructed prior to the effective date of this Act;

### (e)	Political subdivisions that enact a swimming pool barrier ordinance before the effective date of this Act;

### (f)	Political subdivisions that adopt ordinances after the effective date of this Act provided that the ordinance is equal to or more stringent than the provisions of this Act; and

### (g)	A residence in which all the residents are at least six (6) years of age.

## (5)	A person on entering into an agreement to build a swimming pool or contained body of water or an agreement to sell, rent, or lease a dwelling with a swimming pool or contained body of water shall give the buyer, lessee, or renter a notice explaining safety education and responsibilities of pool ownership as approved by the Cabinet for Health Services.

## (6)	A person who violates this section is guilty of a violation except that no fine may be imposed if a sufficient showing is made that the person has subsequently equipped the swimming pool or contained body of water with a barrier pursuant to the requirements in subsection (2) of this section within forty-five (45) days of citation.