# AN ACT relating to methamphetamine contamination.

Be it enacted by the General Assembly of the Commonwealth of Kentucky:

# SECTION 1.   A NEW SECTION OF SUBCHAPTER 1 OF KRS CHAPTER 224 IS CREATED TO READ AS FOLLOWS:

The General Assembly finds that properties are being contaminated with hazardous chemical residues created by the manufacture of methamphetamine. Innocent members of the public may be harmed when they are exposed to these residues if the properties are not properly decontaminated prior to subsequent rental, sale, or use of the properties. Remediation of properties has been frustrated by a lack of comprehensive standards and procedures for decontamination of properties found to have been involved with methamphetamine production. The purpose of this section is to protect public health, safety, and welfare by providing specific cleanup standards and procedures, and authorizing the Department for Environmental Protection of the cabinet to establish a voluntary program that will provide for a property decontamination process that will meet appropriate standards.

## (1)	As used in this section, the following definitions shall apply:

### (a)	"Department" means the Department for Environmental Protection;

### (b)	"Inhabitable property" means any building or structure used as a clandestine methamphetamine drug lab that is intended to be primarily occupied by people, either as a dwelling or a business, including a storage facility, mobile home, or recreational vehicle, that may be sold, leased, or rented for any length of time. The term does not include any water, water system, or sewer system, or land outside of a building or structure;

### (c)	"Surface material" means any porous or nonporous substance common to the interior of a building or structure, including but not limited to ceilings and walls, window coverings, floors and floor coverings, counters, furniture, heating and cooling duct work, and any other surfaces to which inhabitants of the building or structure may be exposed; and

### (d)	"Related hazardous material or hazardous waste" means any hazardous waste as defined in this chapter or hazardous material as defined in KRS 174.405 that is related to the clandestine production of methamphetamine.

## (2)	The decontamination standard for methamphetamine inside inhabitable property is less than or equal to one tenth of one (0.1) microgram of methamphetamine per one hundred (100) square centimeters of surface material, unless the department promulgates an administrative regulation providing for a different standard. The department may provide for other standards by administrative regulation as follows:

### (a)	Standards for precursors to methamphetamine that are consistent with the standard for methamphetamine or standards for related hazardous material or hazardous waste;

### (b)	The number and locations of surface material samples to be collected based on the circumstances of the contamination and acceptable testing methods; and

### (c)	In the absence of an administrative regulation as described in subsection paragraph (b) of this subsection, at least three (3) samples must be collected from the surface material most likely to be contaminated at each property.

## (3)	The department shall promulgate administrative regulations establishing minimum standards for the training and certification of contractors and their employees who are to perform assessments or remediations of inhabitable properties that may be contaminated by methamphetamine residues. If the department conducts such training and testing of contractors and their employees, it may promulgate administrative regulations to provide for the assessment of reasonable fees to cover the costs of the training and testing. The department shall promulgate administrative regulations providing for procedures for certifications of contractors and their employees, and for procedures relating to the decertification of contractors and employees for cause. Administrative regulations may provide for the assessment of reasonable fees to cover the cost of the contractor certification program.

## (4)	Appropriate notice as provided for in this subsection shall occur before agreement to a lease or sale of the inhabitable property. Such notice shall be as follows:

### (a)	An owner of inhabitable property that is known by the owner to have been used as a clandestine methamphetamine drug lab shall notify in writing any subsequent occupant or purchaser of the inhabitable property of that fact, if the inhabitable property has not been remediated to the standards established in subsection (2) of this section by a contractor who is certified in accordance with the provisions of subsection (3) of this section; or

### (b)	Alternatively, an owner or an owner's agent may provide notice to a subsequent occupant or purchaser that the owner or the owner's agent has submitted either:

#### 1.	Documentation to the department by a contractor who is certified pursuant to subsection (3) of this section that the inhabitable property has been remediated to the standards established in subsection (2) of this section; or

#### 2.	Documentation by a certified contractor that the property meets decontamination standards without the need for decontamination procedures.

## (5)	If the department has confirmed that the decontamination standard provided for in subsection (2) of this section has been met, and if a notice has been given as provided for in subsection (4)(b) of this section, the owner and the owner's agent are not liable in any action, based on the presence of methamphetamine or related hazardous waste or material in an inhabitable property, that is brought by a person who has been given notice. The immunity provided for in this subsection does not apply to an owner or an owner's agent who caused the contamination.

## (6)	When a state or local law enforcement agency becomes aware that an inhabitable property has been contaminated by its use as a clandestine methamphetamine drug lab, the agency shall report the contamination to the department and to the local health department. The department shall be responsible for reporting requirements as follows:

### (a)	The department shall maintain a list of inhabitable property that has been reported as contaminated, and the list must be made available to the public through a Web site;

### (b)	Upon confirmation by the department that an inhabitable property has been remediated to the standards established in subsection (2) of this section, or that the inhabitable property meets the decontamination standards without the need for decontamination procedures, the department shall remove the inhabitable property from the list required by paragraph (a) of this subsection;

### (c)	The department shall provide written notification to the local health department and to the property owner of record when the documentation shows that the inhabitable property has been properly assessed or remediated and meets the standards required by subsection (2) of this section.

### (d)	Notwithstanding any other provision of law, when a property has been removed from the list required by this subsection, a property owner, landlord, or real estate agent is not required to report or otherwise disclose past contamination.

## (7)	The department may promulgate administrative regulations to effect the provisions of this section that may not be specified in this section, including the establishment of reasonable requirements for the sufficiency of documentation to be provided by certified contractors.