AN ACT relating to mining.

Be it enacted by the General Assembly of the Commonwealth of Kentucky:

Section 1.   KRS 352.090 is amended to read as follows:

(1)	All unused workings and abandoned parts of mines shall be protected by safeguards that will prevent the accumulation or overflow of gas, and all avenues leading thereto shall be so arranged and conducted as to give warning to all persons of the danger of entering, and notice shall be posted warning all unauthorized persons not to enter these parts of the mine. If the area cannot be adequately ventilated, and examined, or evaluated it shall be sealed in a timely manner.

(2)	No person, except persons authorized to make examination thereof, shall enter any unused or abandoned part of a mine after the warning has been posted.

(3)	Where the practice is to seal abandoned workings, the sealing shall be done in accordance with a mine seal construction plan submitted to the Office of Mine Safety and Licensing. The construction of mine seals according to the mine seal construction plan shall be certified by the mine superintendent after inspection and certification by a licensed engineer. Seal construction shall be done immediately in an effective manner with noncombustible material. In every sealed area, one (1) or more of the seals shall be fitted with a pipe and cap or valve to permit the gases behind the seals to be sampled and also to provide a means of determining any existing hydrostatic pressure. When required by the mine inspector and commissioner, drill holes shall be extended from the surface to the sealed area, or vent pipes shall be extended from the sealed area to a return air course. Sufficient ventilation shall be provided at each seal to prevent dangerous gases from accumulating.

Section 2.   KRS 352.133 is amended to read as follows:

(1)	All underground miners shall be provided with an approved self-contained self-rescuer device and shall have that device within twenty-five (25) feet of them at all times. The self-contained self-rescuer shall be provided to the miners by the licensee at no cost to the miners. The cabinet shall establish requirements for a mine operator to make reports to the Office of Mine Safety and Licensing concerning any self-contained self-rescuer that is inoperative or nonfunctional or that has been removed from service for reasons other than damage associated with normal use.

(2)	In addition to the requirements for self-contained self-rescuers set forth in this section, all licensed premises shall maintain caches of self-contained self-rescuer devices which shall be stored in locations readily accessible to the primary and secondary escapeways or provide proof of an order for self-contained self-rescuers through the submission of a valid purchase order that clearly names the vendor, contact information for the vendor, the number of devices purchased, and the date of the order, which shall not be later than thirty (30) days after July 12, 2006. In all cases, the self-contained self-rescuers shall be in place by July 1, 2007, or shall be extended by the commissioner upon substantiated proof of unavailability.

(a)	The caches shall be maintained in sufficient numbers and locations determined in accordance with the most recent rules, standards, and regulations issued by the United States Mine Safety and Health Administration.

(b)	The caches shall be maintained in storage units capable of protecting the self-contained self-rescuers from water, dust, and any other condition which will cause deterioration of the self-contained self-rescuers.

(c)	The storage unit locations shall have reflective signs that read "SELF-RESCUERS" conspicuously posted as to be visible from the primary and secondary escapeways.[ Intrinsically safe strobe light devices also shall be attached to the storage unit. The strobe light devices may operate continuously or shall be capable of activation in the event of a mine emergency.]

(d)	In addition to the requirements set forth in this section for self-contained self-rescuers, the mine operator shall provide for each person who is underground at least one (1) additional self-contained self-rescuer device which provides protection for a period of one (1) hour or longer, to cover all persons in the mine.

(e)	If a mantrip or mobile equipment is used to enter or exit the mine, additional self-contained self-rescuer devices, each of which provides protection for a period of one (1) hour or longer, shall be available for all persons who use the transportation from portal to portal.

(3)	It shall be a Class D felony for any person to remove a self-rescuer from the cache for purposes other than use during an emergency, or for repair, maintenance, or replacement or as authorized by the licensee.